College of William and Mary

Technology Transfer Office

Title (and Case Number) of Invention

Organic Thiol Stabilizers and Plasticizers for Halogen-Containing Polymers (0608)

Inventors

William H. Starnes, Jr.

Applications

Stabilizers for PVC.  This invention describes a novel organic thiol stabilizer for PVC and other halogenated polymers.

Summary

Dr. Starnes has developed a novel thiol ester stabilizer for rigid and flexible PVC.  A previous invention (W&M 0004) describes numerous other thiol stabilizers.  The compound of the present invention is a highly effective stabilizer for PVC, significantly more effective than other structurally similar compounds.  Perhaps more importantly, this novel stabilizer can be produced inexpensively via a simple condensation reaction between two commodity chemicals (each of which is available for about $2/lb).  The resulting stabilizer can be used to replace hazardous heavy metal compounds currently used to stabilize PVC.

Patent Status

United States Patent No. 7,339,004 (Issued March 4, 2008).

Contact Information

Jason McDevitt (757-221-1751)

jason.mcdevitt@wm.edu